## Slide 1: Bayesian Calibration with Transitional MCMC
Ander Gray, Adolphus Lye, Dominic Calleja, Edoardo Patelli
Ander.Gray@Liverpool.ac.uk

## Slide 2
Who am I?
Msci Physics: Queens University Belfast (2013-2017)
Phd UQ: Uni of Liverpool/ CCFE (2017 – present)
(Working) Thesis: “Uncertainty Quantification in Fusion Neutronics with Imprecise Probabilities”
Mainly interested in:
    Uncertainty Propagation
    Probabilistic Arithmetic
    Dependencies
    Nuclear Data
    Neutron transport MC
    Calibration and V&V
Contact: Ander.Gray@Liverpool.ac.uk
Projects: https://github.com/AnderGray

## Slide 3
Inverse problems
?

## Slide 4
Bayesian updating
Prior:
“knowledge before data”
Pre-calibration
Likelihood:
“compares model to data”
Involves model evaluations
Posterior:
“knowledge after data”
Calibrated model
Evidence:
: Model inputs
: Calibration data
: Prob density
Bayesian probability is a belief, subjective, epistemic uncertainty
is a constant, but unknown
Contrast to randomness, stochasticity, aleatory uncertainty

## Slide 5
Conjugate priors
https://en.wikipedia.org/wiki/Conjugate_prior

## Slide 6
Markov-Chain Monte Carlo
https://chi-feng.github.io/mcmc-demo/
Algorithm for sampling unnormalized distributions
Metropolis-Hastings

## Slide 7
Issues
Metropolis–Hastings struggles with lots of peaks
    When there is lots of data
    Inverse problems are usually non-identifiable
    (lots of solutions/multi-nodal)
Struggles to accept at high dimensions
    Low acceptance rate
    Samples can be highly autocorrelated
    Hard to determine good proposal distribution
Doesn’t give you the evidence
    Model class selection
    Model averaging

## Slide 8
Transitional MCMC
Doesn’t sampling posterior directly
Several steps using easy ”transitional” distributions
- Prior
- Posterior
– selected so change in isn’t dramatic

## Slide 9
Transitional MCMC
Multiple chains used
One chain per sample
Easy to parallelise
Usually low burn-in needed

## Slide 10
Transitional MCMC
Multiple chains used
Uses importance sampling
– likelihood of
= -
Resample according to

## Slide 11
Transitional MCMC
Multiple chains used
Uses importance sampling
Proposal adapted each step
Normal with cov

## Slide 12
Transitional MCMC
Multiple chains used
Uses importance sampling
Proposal adapted each step
Gives estimate of Evidence

## Slide 13
Example
Samples of Gaussians

## Slide 14
Example
Two 20 dimensional gaussians
Sampler gets masses correct

## Slide 15
NASA 2020 UQ challenge
Inputs
Output
5 aleatory parameters
4 epistemic parameters
e

## Slide 16
Parametric model for A
Each marginal will be beta distributed
The joint is created by sampling a random correlation matrix1
1Harry JOE, "Generating random correlation matrices based on partial correlations." Journal of Multivariate Analysis
10 extra epistemic parameters
10 extra epistemic parameters
10 + 10 + 4 = 24 dimensions

## Slide 17
Parametric model for A
20 parameter parametric distribution

## Slide 18
A set of probabilistic models
At t = 2.5s

## Slide 19
Bayesian Calibration with sets of distributions
Bi, Sifeng, Matteo Broggi, and Michael Beer. "The role of the Bhattacharyya distance in stochastic model updating." Mechanical Systems and Signal Processing 117
: distance metric
: “likelihood width”

## Slide 20
Calibrated Model
Betas
Partial Correlations
Original Epistemic
Calibrated output
t = 1 s
t = 2s
t = 3s
t = 4s
t = 5s

## Slide 21
Conclusions
Transitional MCMC can overcome some issues with Metropolis – Hastings
Can sample complicated posteriors
Good in high dimensions (within reason)
Proposal selected by algorithm
Straightforward to parallelise
Gives the Evidence
Python/ Julia package coming in 2021
OpenCossan (MATLAB): General UQ toolbox. TMCMC available in dev branch

## Slide 22
References
Ching, J., & Chen, Y. C. (2007). Transitional Markov chain Monte Carlo method for Bayesian model updating, model class selection, and model averaging. Journal of engineering mechanics, 133(7), 816-832.
TMCMC:
NASA:
Gray, A., Wimbush, A., DeAngelis, M., Hristov, P. O., Miralles-Dolz, E., Calleja, D., & Rocchetta, R. Bayesian calibration and probability bounds analysis solution to the Nasa 2020 UQ challenge on optimization under uncertainty.
Area Metric:
Ferson, S., Oberkampf, W. L., & Ginzburg, L. (2008). Model validation and predictive capability for the thermal challenge problem. Computer Methods in Applied Mechanics and Engineering, 197(29-32), 2408-2430.
Bi, S., Broggi, M., & Beer, M. (2019). The role of the Bhattacharyya distance in stochastic model updating. Mechanical Systems and Signal Processing, 117, 437-452.
2- loop updating:
Contact: Ander.Gray@Liverpool.ac.uk
Projects: https://github.com/AnderGray
Balch, Michael Scott, Ryan Martin, and Scott Ferson. "Satellite conjunction analysis and the false confidence theorem." Proceedings of the Royal Society A 475.2227 (2019): 20180565.
Bayesian false confidence:

## Slide 23
Acknowledgements
Contact: Ander.Gray@Liverpool.ac.uk
Projects: https://github.com/AnderGray
Andrew Davis, Culham Centre for Fusion Energy, UKAEA
Scott Ferson, Institute for Risk and Uncertainty, University of Liverpool
NASA challenge collaborators: Marco De Angelis, Roberto Rocchetta, Alexander Wimbush, Enrique Miralles-Dolz, Peter Hristov, Dominic Calleja
Funding support from EUROATOM and EPSRC, through iCase studentship award and grand agreement No. 633053

## Slide 24
Calculating