## Slide 1: Machine learning in radiation metrology:
Consultancy Meeting on Machine Learning for Nuclear Data
Dec. 9, 2020 ONLINE meeting
Kyushu University (Fukuoka, Japan)
Department of Advanced Energy Engineering Science
Neutron spectrum unfolding and
Gamma-ray spectrometry
Tadahiro KIN

## Slide 2
ML in radiation metrology
Contents
Overview of our ML application
in radiation metrology
ANN Neutron Spectrum Unfolding
Summary
Gamma-ray Spectrometry

## Slide 3
ML in radiation metrology
Self introduction: my research history
１） PhD Course （Kyushu Univ.）
２） 1st Postdoc （JAEA）
３） 2nd Postdoc （JAEA）
４） Assistant / Associate Professor
Cross section measurement of charged particle production by accelerator.
Development of theoretical calculation model (INC and AMD) of nuclear reaction.
Cross section measurement of thermal & cold neutron capture reaction.
Analysis of nuclear level structure.
Exp. at Osaka Univ.
Exp. at JRR-3 & J-PARC （JAEA）
Exp. at FNS & TIARA （JAEA）
Cosmic-ray Muon Radiography (Muography)
Exp. at Kyushu and Tohoku Univ.
RI Production Method by Accelerator Neutron
Exp. can be conducted everywhere on earth
Radiation Measurement
&
Detector Development
Development of Medical RI Production Method by Accelerator Neutron

## Slide 4
ML in radiation metrology
Contents
Overview of our ML application
in radiation metrology
ANN Neutron Spectrum Unfolding
Summary
Gamma-ray Spectrometry

## Slide 5
Today’s Topics
Neutron spectrum unfolding of
multiple-foils activation method
ML
model
Induced activity
24Na: xxx Bq
56Mn: xxx Bq
59Fe: xxx Bq
57Ni: ｘｘｘ Bq
64Cu: xxx Bq
Neutron Energy
Neutron Yield
2. Gamma-ray spectrometry
DDTTNY
Gamma-ray spectrum
Activity
134Cs: xxx Bq
137Cs: xxx Bq
60Co: xxx Bq
152Eu: ｘｘｘ Bq
154Eu: xxx Bq
ML in radiation metrology
ML
model

## Slide 6
muon
electron
Today’s topics (details skipped)
3. Measurement of terrestrial cosmic-ray muon
spectrum around low energy range
ML
model A
(classification)
ML in radiation metrology
Single event
deposit energies
1st layer: xxx MeV
2nd layer: xxx MeV
3rd layer: xxx MeV
…
Plastic
Scintillators
Iron
Absorber
discard
(20% of total events)
ML
model B
(regression)
Kinetic energy: yyy MeV
Application of Japanese Patent
特願2019-160460 (Sep. 3, 2019)
Deposit energy pattern is dependent to particle type and its energy.
Full-Absorption Muon Energy Spectrometer+ (FAMES+)

## Slide 7
ML in radiation metrology
Contents
Overview of our ML application
in radiation metrology
ANN Neutron Spectrum Unfolding
Summary
Gamma-ray Spectrometry

## Slide 8
ML in radiation metrology
ANN Neutron Spectrum Unfolding: Background
Reactor-based Method:
  Produced by neutron irradiation or fission products
Conventional Methods
+
59Co
(stable)
n
+
60Co
(radioactive)
n
235U
99Mo
Accelerator-based Method:
  Produced by charged particle induced reactions
Proton
Accelerator
Protons
18O
18O + p → 18F + n

## Slide 9
ML in radiation metrology
ANN Neutron Spectrum Unfolding: Background
Deuteron
Accelerator
Neutron
Converter
Thick target made of C or Be
Deuterons
Neutrons
Raw
Material
Medical RI
Separation, Extraction
Accelerator based
Domestic Production
→ Stable supply system
Deuteron induced neutron → High intensity
Adjustable neutron energy distribution
→ high purity, efficient
Fast Neutron
New production route
→ Longer half-life PET
→ New therapeutic RI
Irradiation material
→ Large amount
→ Free chemical form
Production route of charged particle reaction
The route of
neutron induced RI
Charged
Particle
Neutron
Cross section multiplied twice,
but comparable amount can be produced, because large amount of target can be used.
Part of Generation of Radioisotopes with Accelerator Neutrons by Deuterons, Y. Nagai et al., J. Phys. Soc. JPN, 82, 064201 (2013).

## Slide 10
ML in radiation metrology
ANN Neutron Spectrum Unfolding: Objective
e.g., High purity 64Cu production T. Kin, et al., J. Nucl. Sci. Tech. 54 (2017) 1123.
  for estimation of production amount, impurities,
  and design of irradiation system
Our 1st ML application
(IEEE NSS/MIC 2017)
  Multiple-foils activation method. → Unfolding process
    Development of ANN unfolding code (2016)
Using very simple ANN model,
but has sufficient performance.
AVF930 Cyclotron, CYRIC, Tohoku Univ. (JPN)
Using no open library (for our education)
Systematic nuclear data measurement of DDTTNY via the C and Be (d,n) reactions

## Slide 11
ML in radiation metrology
ANN Unfolding Code
Multiple-foils activation method
deuteron
multiple foils
C or Be
thick target
Placed from 0 to 75deg. (in15deg. step)
Al
Co
Zr
Au
Ni
Zn
Mo
Fe
2cm
1cm
Irradiation foils
Precise absolute value:
Based on a lot of reliable integral experiments. Detectors are uniform (determined by natural abundance).
Precise angular-differential TTNY:
Irradiation of all angles at same time. Beam current measurement.
Low energy resolution:
No problem, because both DDTTNY and neutron excitations of focused reactions are smooth.
Output of the method is numbers of produced atoms measured by gamma-ray spectrometry
Unfolding Process
Energy-differential neutron yield

## Slide 12
ML in radiation metrology
ANN Unfolding Code
Neutron spectrum unfolding
Yield at EOI
Obtained by gamma-ray spectrometry
Response function
using nuclear data library
JENDL-4.0 or EAF2010
DDTTNY
to be derived
TTNY
Constant
Initial Guess DDTTNY
Unfolding
solving inverse problem
If needed, calculated DDTTNY by DEURACS* was used.
(Note that our ANN code not requires)
*S. Nakayama et al. Phys. Rev. C 94, 014618 (2016).
: ID of activated nuclide
: Cross section
: Surface No. density of target
: Total beam charge
: Decay constant
: Solid angle
: Irradiation time
No. of focused reaction No. of neutron energy group
→ ill-posed problem (cannot derive analytically)

## Slide 13
ML in radiation metrology
ANN Unfolding Code
Developed ANN unfolding code
Simple fully-connected feedforward neural network is sufficient ← independent input data & one-dimensional output

## Slide 14
ML in radiation metrology
ANN Unfolding Code
Developed ANN unfolding code
No open ML library used (not to be a black box user)
Training data (self-producible gaussian + EXFOR)

## Slide 15
ML in radiation metrology
Results and discussion
GRAVEL (SAND-II upgrade ver.)：
Conventional unfolding code.
having more than 50 years history.
(broken lines)
GRAVEL code requires initial guess DDTTNY and convergence condition should be artificially determined.
Present ANN-based code requires no initial guess and convergence condition but has same performance with GRAVEL.
ANN：
Present results (solid lines)

## Slide 16
ANN
GRAVEL
27Al(n,a)24gNa
58Ni(n,p)28gCo
56Fe(n,p)56Mn
197Au(n,2n)196Au
197Au(n,g)198Au
59Co(n,a)56Mn
ML in radiation metrology
Results and discussion
Folding calculation (C) over activity obtained in the experiment (E).
Average Standard Deviation of C/E for all reactions and angles:
  ANN: 21.1 % (19.4% w/o 197Au(n,g))
  GRAVEL: 31.3% (15.8% w/o 197Au(n,g))

## Slide 17
ML in radiation metrology
Contents
Overview of our ML application
in radiation metrology
ANN Neutron Spectrum Unfolding
Summary
Gamma-ray Spectrometry

## Slide 18
ML in radiation metrology
Gamma-ray Spectrometry: Background
Gamma-ray spectrometry by ML
Release to the air
Fallout
Direct pollution
of agricultural crops
Accumulation to bed
Leakage to the sea
Leach into groundwater
Absorption and diffusion to soil
Spreading by
Meteorological
phenomena
Barn animal
Distant
area
Fukushima Daiichi Nuclear Plant Accident
Huge number of samples must be measured,
and in many cases, the sample has low activity.
  → To confirm “ND,” long measurement time is required.
Key is “automation “ and “rapidity.” … ML has potential.

## Slide 19
ML in radiation metrology
Gamma-ray Spectrometry: Methods
Conventional Method: Covell Method
Simple linear estimation method to subtract background component under an interested photo peak
  → implemented on all gamma-ray spectrometry software.

## Slide 20
ML in radiation metrology
Gamma-ray Spectrometry: Methods
How can we reduce measurement time?
As long as using only photo peak, no method drastically improve measurement time of Covell method.
Ge detector efficiency
If discarded events in Covell method can be taken into account, 3 times faster measurement is possible (ideally).
511 keV
(annihilation)
662 keV
(137Cs)
UNFOLDING!!
Once we achieved around 10 times faster measurement of NaI(Tl) gamma-ray spectrometry by the iterative unfolding method (awarded by Minister of the environment of Japan in 2015)
Any codes are okay, but we have experience of successful unfolding by ML model (as shown before).

## Slide 21
ML in radiation metrology
Gamma-ray Spectrometry: Methods
Spectrum “shape” has information
→ Convolutional Neural Network (CNN) is promising.
Photo peak
Compton component ends
Doublet

## Slide 22
Convolution
Convolution
Pooling
Pooling
Pooling
ML in radiation metrology
Gamma-ray Spectrometry: Methods
R. Takahashi (M1 student) coded everything last year for his bachelor thesis
Tensorflow + keras
to develop the ML model
Using GPU server machine
having 2 boards of Geforce RTX 3020
Loss: MSE
Activity prediction of 137Cs including 134Cs and 40K
(random activity for each nuclide, fixed measurement time 60s)
Training and validation data sets were prepared by Geant4 simulation
137Cs
Activity

## Slide 23
ML in radiation metrology
Results and discussion: 137Cs
Covell method
Present CNN model
Measurement time of the data set was fixed to 60 sec.,
thus the following analysis method proposed
Derive squared value of ratio of SD:
Preliminary
Preliminary
SD for Covell method is determined by statistical uncertainty of the photo peak.
The statistical uncertainty reduces with measurement time.
If “” times longer measurement is preformed, the SD reduces from to.
Therefore, “” can be regarded as measurement time increasing factor of the CNN model.

## Slide 24
ML in radiation metrology
Results and discussion: 137Cs activity
What does “” mean?
By analyzing with Covell method, “” times longer measurement time is necessary. It can be regarded as time increasing factor.
Larger than 1 for is expected and higher activity range (~1.5), we achieved. However lower range did not…
→ Cost (loss) function development has continued…
Preliminary

## Slide 25
ML in radiation metrology
Contents
Overview of our ML application
in radiation metrology
ANN Neutron Spectrum Unfolding
Summary
Gamma-ray Spectrometry

## Slide 26
ML in radiation metrology
Summary
ML application for neutron spectrum unfolding of
multiple-foils activation method
Simple fully-connected feedforward NN model
  gives sufficient unfolding results compared with those of conventional one,
  even it requires no initial guess and human inducible convergence condition.

## Slide 27
ML in radiation metrology
Summary
Gamma-ray spectrometry
Covell method
CNN model
Convolutional Neural Network
  may use also non-photo peak events for higher activity samples,
  may not directly count photo-peak events, considering the worse performance around lower activity sample.
Preliminary

## Slide 28
ML in radiation metrology
Covell method
CNN model
Preliminary
Thank you for your attention.
Questions and/or Comments?
Tadahiro KIN, Kyushu Univ. (Japan)
e-mail: kin.tadahiro.981@m.kyushu-u.ac.jp