## Slide 1
R. Capote (IAEA) and A. Trkov (JSI)
On behalf of the INDEN collaboration
https://www-nds.iaea.org/INDEN
INDEN evaluation of Fe isotopes &
the 55Mn update of thermal (n,γ) gammas

## Slide 2
Si(n,n’γ)
Hint:
ENDF/B-VI.8
was better for gammas
Marie-Laure Mauborgne et al, CSWEG 2019 & EPJ WoC 239 (2020) 20007 (ND2019)
Problems identified in inelastic/capture gammas of many ENDF/B-VIII.0 evaluations

## Slide 3
Marie-Laure Mauborgne et al, CSWEG 2019 & EPJ WoC 239 (2020) 20007 (ND2019)
Problems identified in inelastic/capture gammas of many ENDF/B-VIII.0 evaluations
Hint:
ENDF/B-VI.8
was better for gammas
56Fe(n,γ)

## Slide 4
Marie-Laure Mauborgne et al, CSWEG 2019 & EPJ WoC 239 (2020) 20007 (ND2019)
Problems identified in inelastic/capture gammas of many ENDF/B-VIII.0 evaluations
Similar problems:
Si(n,n’γ),
Fe(n,γ), Fe(n,n’γ),
Mg(n,γ), Mg(n,n’γ), Ti(n,γ), Ti(n,n’γ)
Hint:
ENDF/B-VI.8
was better for gammas

## Slide 5
Problems discussed, but not solved

## Slide 6
55Mn update of thermal (n,γ) gammas
55Mn - case study of the problem
New INDEN files

## Slide 7
EGAF lines superimposed on a
calculated continuum
Thermal capture photon spectrum updated
See description in INDC(NDS)-0810, performance restored
55Mn update of thermal (n,γ) gammas
EGAF IAEA database:
Measured thermal capture γ
Quite challenging to
reproduce via modelling
But very well measured ,
Let’s use it.

## Slide 8: 55Mn update of thermal (n,g) gammas
Mn-55 evaluation in ENDF/B-VIII.0 was criticized for poor prediction of capture gamma spectra (Marie-Laure Mauborgne, CSEWG-2019, EPJ WoC 239, 20007 (2020).
The data are important for oil-well exploration.
Using the information in the EGAF library and EMPIRE nuclear model calculations the gamma production data were improved. High resolution energy bins (~5 keV/bin)
Good performance of updated file mn55e80p on proprietary benchmark was confirmed by Marie-Laure Mauborgne
Documented in INDC(NDS)-0810 on "Evaluation of thermal capture gamma spectra"

## Slide 9
Fig. 32, 35, Nuclear Data Sheets,148 (2018) 214-253
Problems with ENDF/B-VIII.0 (CIELO) 56Fe
Up to 30% underestimation of neutron leakage for En=1-4 MeV

## Slide 10
56Fe evaluation
New measurements 56Fe(n,el)
E. Pirovano et al, JRC Geel

## Slide 11
Fe 14 MeV – problem
Indep. confirmation
Polyethylene (C2H4)n
Ф13 cm×6 cm
Ф13 cm×6 cm
Ф13 cm×6 cm
Fe
Fe
Y. Ding et al, EPJ WoC 239 (2020) 18010 (ND2019)

## Slide 12
B. Jansky et al., CVR, Rez, Czechia,EPJ WoC 239 (2020) 18005 (ND2019)
252Cf(sf) neutron leakage: 100 cm sphere
Note that ENDF/B-VIII.0 Fe = CIELO
H-proportional detector (HPD)
stilbene detector
Up to 30% overestimation of neutron leakage for En~300 keV

## Slide 13
(n,el) minima poorly described (27 keV,~300keV, ...)
Sensitive to transmission through thick samples (>5 cm)
Patching the Fe-56 evaluation: EL (1)
Adhoc increase, NO fit

## Slide 14: INDEN Fe: Filling the elastic cross-section minima (relevant for deep penetration problems only) Solution already tested and suggested by M. Diakaki

## Slide 15
B. Jansky et al., CVR, Rez, Czechia,EPJ WoC 239 (2020) 18005 (ND2019)
252Cf(sf) neutron leakage: 100 cm sphere
Note that ENDF/B-VIII.0 Fe = CIELO
H-proportional detector (HPD)
stilbene detector
.
.
Notes: A very crowded table?

## Slide 16
Patching the Fe-56 evaluation: TOTAL

## Slide 17
New INDEN files
Patching the 56Fe evaluation:
(n,inl)

## Slide 18
Patching the Fe-56 evaluation: EL (1)

## Slide 19
Patching the 56Fe evaluation:
(n,inl)

## Slide 20: Improvements to 56Fe evaluation
Total cross sections are trusted
New measurements by E. Pirovano at IRMM support a higher elastic cross section
Capture is too small to play a role
Conclusion: measured inelastic likely too high
Inelastic cross section was scaled down by 10-15%, assigning the difference to elastic (exact comparison of cross sections is difficult due to strong fluctuations)
Elastic minima were filled to reproduce observed transmission. A proper R-matrix fit will be appreciated.
Older thermal capture needs to be likely restored

## Slide 21: Normalization issue ? Wu H., ND2019

## Slide 22
Ratio to -B/VIII.0

## Slide 23: Future improvements of (n,inl)

## Slide 24: Future improvements: M. Diakaki
to do
1/v backg = Direct capture ?

## Slide 25: Changes to 56Fe evaluation: (nth,g)
Thermal capture JEFF-3.2 = 2.586 b
Thermal capture ENDF/B-VIII.0
= 2.605b (+0.7% rel. to JEFF-3.2)
Firestone et al, Phys. Rev. C95 (2017) 01428
= 2.3940.019b (-8.0% rel. to JEFF-3.2)
Criticality benchmarks show mixed results (AT)
What is the truth?

## Slide 26: Validation of the 56Fe thermal capture

## Slide 27: Validation of the 56Fe thermal capture

## Slide 28: Changes to 56Fe evaluation: (nth,g)
Thermal capture JEFF-3.2 = 2.586 b
Thermal capture ENDF/B-VIII.0
= 2.605b (+0.7% rel. to JEFF-3.2)
Firestone et al, Phys. Rev. C95 (2017) 01428
= 2.3940.019b (-8.0% rel. to JEFF-3.2)
MAESTRO result:
(C/E-1) Fe = +0.3 (1.1)%
(C/E-1) SS316L (64% Fe, 18%Cr) = -0.7 (1.2)%
Firestone et al (nth,g) reduction is not acceptable (>5 away)

## Slide 29: Conclusions
INDEN interactions strongly helped to find deficiencies in existing evaluations and highlight potential solutions to existing challenges: https://www-nds.iaea.org/INDEN/
Reduced inelastic in Fe-56 deserves further experimental and/or theoretical investigations
New R-matrix fit that reproduces fitted minima of the elastic cross-section of Fe-56 desirable and includes direct capture (1/v and above 300 keV)
Additional work needed on inelastic, RRR fits, thermal capture gammas
Updated evaluations for Mn-55, Fe-56, and Fe-57 (inelastic) are available for testing.
See Trkov presentation for additional validation
Mn-55 updated evaluation was tested on a relevant proprietary benchmark. Significant improvement was demonstrated.

## Slide 30
DA fluctuations and smoothing: P0 (E)  el

## Slide 31
DA fluctuations and smoothing: P1(E)  el

## Slide 32
DA fluctuations and smoothing: P2(E)  el

## Slide 33: DA: 500 keV
DA: 500 keV
DA: 800 keV
DA: 800 keV