## Slide 1: Decompensating effects in nuclear data integral benchmarking: How to tag a specific xs ? example of 238U(n,n’), p(n,p) and 235U (or 239Pu) PFNS
September 28, 2015@IAEA
David BERNARD

## Slide 2: OUTLINE: A recent example
Project oriented approach GEN-III + GEN-IV (ND uncertainties propagation)
Needed reduction of the number of Degree Of Freedom: Tag a specific XS (or ND in general) by using integral separate effects.
Perform new integral dedicated experiments (recent example)

## Slide 3: Project oriented approach GEN-III+IV (ND uncertainties propagation)
  238U covariance matrices amongst international evaluations (ENDF/B-VII, JENDL-4, TENDL-2009, French-COMAC) are not consistent
  A 15% standard deviation, constant with neutron energy, seems realistic
French COMAC covariance
COMMARA-2 covariance
Constant =15%
238U(n,n’) covariance matrices

## Slide 4
Total uncertainty: 5.3% @1s is more than the required target accuracy (1%) on PWR power map calculation.
238U(n,n’) takes 85% of this overall uncertainty.
Project oriented approach GEN-III+IV (ND uncertainties propagation) OECD/UAM
+ around 3 to 4% for 235U PFNS !!!!!

## Slide 5
First set: critical spheres (Radius r1) with fissile material
Second set: critical spheres (Radius r2) with the same fissile material are reflected by 238U
First order perturbation theory shows that the sensitivity to this reflector saving (r2-r1<0) can be expressed as SReflector = S(G)= Sr2 –Sr1
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking

## Slide 6
Proof by deterministic calculations:
Constraint by JEZEBEL keff uncertainties
639pcm/% = DExp / DPu239 → DPu239 = 200 / 639 ≈ 0.3%
Then, the reflector saving uncertainty due to 239Pu is about:
DG= 50pcm/% * 0.3% = 15 pcm.
S(G,238U) = S(G,238U(n,n’g)+(n,n))
+ S(G,238U(n,f)+c+n)
+ S(G,238U(n,g))
+ S(G,238U(n,xn))
-110pcm/%
+115pcm/%
-36pcm/%
+2pcm/%
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking

## Slide 7
Large core keff: Big-10
Infinite core keff=k=1.0: SCHERZO+MINERVE+SNEAK8
(235U/238U=6.7% enrichment is needed to be just critical for infinite geometry)
avoiding so the sensitivity to Secondary Angular Distributions !!!
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking

## Slide 8
Integral Exp. with strong sensitivity to 238U(n,n’) are :
  Reactivity worth of natU reflectors
      LANL U235 spheres
      Godiva bare sphere(HMF-001)
      Topsy(HMF-002), Flattop (HMF-028)
      Russian Pu spheres
      PMF-022, PMF-041, PMF-020
      LANL Pu spheres
      PMF-001, PMF-010, PMF-006
  Fast reactors with metallic U slightly-enriched fuel
      SCHERZO : K∞ = 1 (Minerve + Sneak)
      BIG-TEN : large critical core 10%235U
  fU238/fU235 spectral index in U media
  (SCHERZO, ERMINE, BIG-TEN)
BIG-TEN: TRIPOLI4 geometry
VNIITF reflected Sphere
Fissile Pu sphere
Udepleted
reflector
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking

## Slide 9
3D flux measurements in large PWRs :
   Fission Chamber measurements at BOL HZP start-up : French N4 1500 MWe
N4 Radial cut
TRIPOLI4 geometry
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking

## Slide 10
Needed reduction of the number of Degree Of Freedom:
Integral trend tracking
238U(n[2;5]MeV,n’g) cross section (including so double differential XS)
seems to be overestimated by about (11±3)% in JEFF-3.1.1.
(note that a priori uncertainty was about 15%)
This result is not that much sensitive to correlation matrix.
Important remark: This trend is confirmed whatever the a priori uncertainty of 238U is

## Slide 11
STEP3: confirm ND trend
Perform new integral dedicated experiments (recent example)

## Slide 12: Principle OF the excalibur experiment
Transmission values measured by dosimeter detectors are linked to inelastic XS.
F(X) accounts for multiple scatterings

## Slide 13: Principle OF the excalibur experiment
   Reduced degree of freedom compared with other integral experiments
  - much smaller sensitivity to the prompt fission neutron spectrum
  - negligible contributions from 235U or 239Pu cross sections
  Proof by Monte Carlo sensitivity calculations (direct calculations by modification of ENDF files)

## Slide 14: Experimental devices and set-up description
The highly Enriched Uranium non reflected core of CALIBAN (CEA Valduc) was a metal fast burst reactor (like the GODIVA reactor in US). It provided a quasi fast prompt fission neutron spectrum to a set-up made of natU from which transmission measurement are performed.

## Slide 15: Experimental devices and set-up description, first phase; the Sphere

## Slide 16: Experimental devices and set-up description, second phase; cylinders
Transmission material: 2 cylinders made of natU (40kg each) located approximatively at 50cm from the center cavity of CALIBAN.
3 positions, X1 (entrance), X2 (middle) and X3 (exit) aim at measuring 3 neutron transmissions:
Transmission by the first cylinder: T(1X)
Transmissions by the two cylinders: T(2X)
Transmissions by the second cylinder only: T(2X)/T(1X)

## Slide 17: Experimental devices and set-up description
Two irradiations on the same week (2hours@600W) were performed with two series of dosimeters:
First irradiation: 3 Ni, 3 Fe, 3 Rh and 3 U8 dosimeters for transmission measurements and 1 U8 dosimeter for estimating the decay time correction
Second irradiation: 3 In, 3 Ti, 3 Mg, 2 U5 and 3 U8 dosimeters for transmission measurements and 2 U8 and 1 U5 dosimeters for estimating the decay time correction.
“E50%” stands for the median energy for individual dosimeter reactions induced by a 252Cf spontaneous neutron fission source

## Slide 18: Rough data and first experimental results
Dosimeter activities were counted using g-spectrometry
All measurements were duplicated in time (and were done sometimes in different laboratories, involving different teams, detector geometries, acquisition chains and software).
Including net Count rate during the active acquisition time Dta.
75 transmissions measured (±3%) !!
Interpretation is on-going !!!
Leading to reach the targeted accuracy

## Slide 19: Not the end of the story !!!!
Improving 238U(n,n’) is needed but is maybe not enough.
Modifications of 235U PFNS impact integral calculations…not in the good direction sometimes….
Soften PFNS is neutronically equivalent
to increase high energy neutron scattering !!!!
Both are strongly linked in integral analysis…except for transmissions experiments

## Slide 20: ANOther example for a needed decompensation
For a very long time, ICSBEP/PST solutions are supposed to be sensitive to 239Pu thermal and subthermal h value. That’s fully right !!!! But to neutron leakage as well…(PFNS + scattering at high energy)

## Slide 21: Other example for a needed decompensation
In the Fermi equation,
the migration area is D/a !!
For small systems, the keff and so the leakage rate is sensitive to chronologically speaking for the neutron:
Its born PFNS
238U inelastic scattering (outgoing energy 300keV in average) if any
1H and 16O elastic scattering in the 100keV-1MeV highly sensitive region where a 2% uncertainty is observed !!!

## Slide 22: Decompensating XS effects
New experiments to be done:
Fast neutron transmission in
Hydrogen media
Oxygen media
PFNS has to be well assessed at the same time (mean value AND uncertainties see dosimetric activities in the dedicated CRP@IAEA)

## Slide 23: CONCLUSIONS
Nuclear Data analysis of PST-keff, Void effect, Doppler, beff in FBR, power map in PWR… are suffering to ND compensation (XS, PFNS)
Specific isotope transmission experiments are needed to decompensate effects.
The goal is to improve ND evaluations and to give constraints on covariances as well !