## Slide 1: GAIA : Nuclear data processing for transport and criticality safety calculations at IRSN
Luiz Leal, luiz.leal@irsn.fr
Wim Haeck, wim.haeck@irsn.fr

## Slide 2: Outline
Introduction
GAIA 1.x.x
  Processing path
  Library QA procedures
GAIA 2
  Overview and features
  Application

## Slide 3: Validation of neutronic simulations
Nuclear Data
Integral Experiments
Software
GAIA 1.x.x
GAIA 2
ND Processing
MORET5
VESTA
Transport
MACSENS
BERING
S/U Analysis
Application system keff + dkeff

## Slide 4: Nuclear data processing using GAIA
GAIA 1.x.x : An NJOY wrapper for data library QA
  Uses either NJOY 99 or NJOY 2012
    Inherently limited to ENDF formatted files
  Current tool for application nuclear data library generation
  Libraries for MORET5, MCNP(X) and VESTA : ACE and PENDF files
GAIA 2 : a nuclear data manipulation software framework
  Multiple ways of using the software
    As a standalone application
    As an integrated component in other applications (e.g. VESTA 3)
  Capable of reading and writing to and from various formats
    ENDF, GND, ACE and other formats
  Provide collaborative development without “heavy” source licenses

## Slide 5
GAIA 1.x.x : An NJOY wrapper with QA

## Slide 6: Making application libraries
Before nuclear data can be used it needs to be processed
  Multiple tools exist: NJOY, PREPRO, AMPX
  Degrades data and renders it code dependent (CE versus MG, etc.)
3 essential steps in preparing a library:
  The library processing has been verified
    NJOY processing path selection – justify and document everything
    Examine NJOY output – understand everything and act accordingly
    Perform other necessary tests – act accordingly
  The library needs to be validated for use
  Everything needs to be documented
    NJOY is not a black box and should not be treated as such!

## Slide 7: Processing path in GAIA 1.x.x

## Slide 8: Processing path in GAIA 1.0.0x
moder
20 -25
reconr
-25 -21
'AM241 - 293.6 K - JENDL 4.0 (NJOY 99.259)'/
9543 0 0
0.001 0 0.01 5e-08
0 /
broadr
-25 -21 -22
9543 1 0 0 0
0.001 1e+06 0.01 5e-08
293.6
0 /
moder
-22 30
heatr
-25 -22 -21 /
9543 5 0 0 0 0 /
302 318 402 442 444 /
heatr
-25 -22 -23 /
9543 6 0 1 0 2 /
302 303 318 402 442 444 /
thermr
0 -21 -22 /
0 9543 16 1 1 0 1 221 2 /
293.6
0.001 5.0
gaspr
-25 -22 -21 /
unresr
-25 -21 -22
9543 1 9 1
293.6
1e+10 1e+8 1e+6 1e+4 1e+3 3e+2 1e+2 3e+1 1e+1
0 /
purr
-25 -22 -21
9543 1 9 20 64 1 0
293.6
1e+10 1e+8 1e+6 1e+4 1e+3 3e+2 1e+2 3e+1 1e+1
0 /
acer
-25 -21 0 40 41
1 0 1 .02 /
'AM241 - 293.6 K - JENDL 4.0 (NJOY 99.259)'/
9543 293.6
1 1
/
acer
0 40 42 40 41
7 1 1 -1 /
'AM241 - 293.6 K - JENDL 4.0 (NJOY 99.259)'/
viewr
42 43
stop

## Slide 9: Library QA : NJOY output
An NJOY output file contains a wealth of useful information:
  The RECONR resonance reconstruction error estimation
  Various messages or errors to inform the user of certain situations
  Output from the HEATR run for kinematic checks
  Data from UNRESR that can be used to check results from PURR
  And last but not least: the ACE consistency checks
It is important to understand everything and act accordingly when a problem is detected.

## Slide 10: Library QA : NJOY output
Something is wrong with this output for elemental sulphur
  Can you guess what it is?
  The original evaluation dates back to 1979, as old as I am
estimated maximum error due to
resonance integral check (errmax,errint)
upper elastic percent capture percent fission percent
energy integral error integral error integral error
1.00E-05
1.00E-04 2.26E+00 0.000 3.58E+01 0.000 1.24E-01 0.000
1.00E-03 2.26E+00 0.000 1.13E+01 0.000 3.92E-02 0.000
1.00E-02 2.26E+00 0.000 3.58E+00 0.000 1.24E-02 0.000
1.00E-01 2.26E+00 0.000 1.13E+00 0.000 3.92E-03 0.000
...
1.00E+05 1.10E+00 0.003 1.53E-03 0.038 2.01E-03 1.743
2.00E+05 5.86E+00 0.001 2.04E-03 0.247 1.30E-03 1.077
5.00E+05 2.48E+00 0.010 1.22E-03 0.866 6.59E-04 1.765
1.00E+06 1.52E+00 0.018 5.29E-04 1.057 2.69E-05 2.025
Elemental sulphur with a non zero fission integral?
It is not because it runs that it is correct.

## Slide 11: Library QA : NJOY output
The case of non-positive elastic cross sections – RECONR:
  ---message from emerge---nonpositive elastic cross sections found.
  Due to resonance reconstruction and effects the following:
    JEF 2.2: 61Ni, 128Te, 152Eu, 154Eu, 157Gd, 176Lu, 185Re, 240Pu, 241Am, 244Cm
    JEFF 3.1: 40Ar, 61Ni, 111Cd, 113Cd, 128Te, 157Gd, 182W, 244Cm
    ENDF/B-VI,8: 56Fe, 57Fe, 61Ni, 74Se, 78Kr, 80Kr, 84Kr, 84Sr, 111Cd, 113Cd, 112Sn, 114Sn, 230Th, 238Pu, 242Pu, 244Pu , 242Cm, 244Cm, 248Cm, 250Cf, 252Cf
  What should you do?
    Plot it to see how “bad” it is
    Look at the other cross sections to see the overall influence

## Slide 12: Library QA : ACER consistency tests
The case of 11B from JEFF 3.1: No problems found
ace consistency checks
----------------------
check reaction thresholds against q values
check that main energy grid is monotonic
check angular distributions for correct reference frame
check angular distributions for unreasonable cosine values
check energy distributions
check photon production sum
check photon distributions
checking particle production sections
proton production:
checking energy distributions
alpha production:
checking energy distributions
no problems found

## Slide 13
GAIA 2 : A nuclear data processing software framework

## Slide 14: Objectives
GAIA : a nuclear data manipulation software framework
  As a standalone application
  As an integrated component in other applications
Objectives
  Library generation for current (ACE and PENDF) and future tools
  Capable of reading from multiple nuclear data evaluation formats
    ENDF, GND and future formats
  Manipulation of data outside of the scope of existing tools
    Resonance reconstruction & Doppler broadening in a single step
    Thermal scattering data
    DPA and heating cross sections
  Provide collaborative development without “heavy” source licenses

## Slide 15: Using GAIA as a standalone tool
In short: sequential modules using an internal data object for information exchange

## Slide 16: Using GAIA inside other software
In short: to manipulate the data or make it compatible with what the software needs

## Slide 17: GAIA features
Prototyping and method development for independent capabilities at IRSN (G. Ferran and W. Haeck)
  Resonance reconstruction based on R-matrix formalism
  Multiple options for Doppler broadening including reconstruction
    Fast Fourier transformations
    Gauss quadrature
  Calculation of angular dependent cross-section data from resonance parameters (Blatt and Biedenharn formalism)
Future developments
  Unresolved resonance treatment
  Thermal scattering law treatment - S(α,β)
  Uncertainty processing: variance and covariance

## Slide 18: GAIA features
RECONR
BROADR
GAIA 2
PURR
ENDF
ACER
ACE Library

## Slide 19: GAIA features
R-Matrix
Single-Level Breit-Wigner
Multi-Level Breit-Wigner
Adler-Adler
Reich-Moore
Multipole
R-Matrix Limited: ENDF format

## Slide 20: GAIA features

## Slide 21: Application
Benchmark: ALARM-CF-FE-SHIELD-001 – ICSBEP – IPPE, Russia
  Neutron and photon leakage spectra from Cf-252 source
  Six iron spheres of diameters of 20, 30, 40, 50, 60, and 70 cm

## Slide 22: Application