## Slide 1: Current nuclear data processing status of JAEA
JAEA
Research Group for Reactor Physics and Standard Nuclear Code System
Kenichi Tada

## Slide 2: Contents
Answer of Questionnaire
Request for New Nuclear Data Processing Code
Other

## Slide 3: Q1 What is the end purpose of your data processing activities?
JAEA develops many nuclear calculation codes
  Deterministic code
    SRAC (for thermal reactor), SLAROM-UF(for fast reactor)
  Continuous energy Monte Carlo (MC) code
    MVP (for reactor calculation), PHITS (for shielding calculation)
To distribute the cross section libraries for above nuclear calculation codes, JAEA uses the nuclear data processing code
  Cross section libraries based on JENDL, ENDF/B and JEFF are prepared.

## Slide 4: Q2 Which application code uses your processed data?
JAEA uses NJOY99 and PREPRO codes
  To appropriately process JENDL, some modules must be modified
NJOY2012 is also used for test processing
  NJOY2012 is not allowed to release the cross section library processed with modified code
  NJOY2012 has still some bugs, which are not officially fixed soon as told and we also modify NJOY2012 for JENDL
    For example, it took 1.5 year to update NJOY2012 from patch 8 to patch 50.
  For these reasons, It is difficult to make cross section libraries for publication

## Slide 5: Q3 What is the processed data format?
Deterministic code : Original data format
  SRAC : 107 groups structure
  SLAROM-UF : 70, 175 and 900 groups structure
Continuous energy MC code
  MVP : Original data format
  PHITS : ACE format

## Slide 6: Q4 What are the characteristics of the group structure for deterministic codes? (for SRAC)
Current SRAC code (107 groups)
  Fast group : Equal lethargy width
  Thermal group : Finer than equal lethargy width
    The detail concept of the group structure is unknown
    Developers were already retired
New SRAC code (200 groups)
  Similar to 172 groups XMAS energy groups structure
  Some energy boundaries are added
    Iron cross section variation is appropriately treated
    To improve the prediction accuracy of the shielding calculation

## Slide 7: Q4 What are the characteristics of the group structure for deterministic codes? (for SLAROM-UF)
70 groups structure
  Equal lethargy width
175 groups structure
  Similar to 174 groups VITAMIN energy groups structure
    Add energy boundary at 12.84 MeV
900 groups structure
  Equal lethargy width
  Considering the average lethargy increased by the elastic scattering of 238U
    Less than 50 keV : lethargy width is 0.050-0.120
    Larger than 50 keV : lethargy width is 0.008

## Slide 8: Q5 What is the status of your data processing code?
Currently, JAEA uses NJOY99 and PREPRO codes

## Slide 9: Q6 If enhancement of the open-source data processing capabilities is undertaken through the IAEA, are you willing to contribute your software?
It is difficult to contribute the development of the open-source code
  Contribution to the open-source project may not be recognized as JAEA’s work
  JAEA may not allow to collaborate on the open-souce project
We may contribute as a benchmark problem
  Comparing the cross section data library
  Comparing the keff or reaction rate in some cases

## Slide 10: Q7 Which in your opinion are the data processing modules of highest priority that are not available as open-source software?
None
  If the open-source software permits the modification of the source code
Many neutron calculation code vendors add their own functions or use their original cross section data format
  These functions and data format are non-disclosure information
  The open-source software should be allowed the modification of the source code with no restriction

## Slide 11: Requests for New Nuclear Data Processing Code
  For function
    Following the designation of the evaluated nuclear data library
  Enhancement of data output tool
For processed data format
  Standardization of cross section data format

## Slide 12: Following the designation of the evaluated nuclear data library
When JENDL-4.0 is processed by NJOY99 code, some modules process as unintended
  The Doppler broadening process is stopped at very low energy in some nuclei
    235U, 64Zn, 57Fe, etc.
  The thermal scattering low process ignores interpolation type written in the evaluated nuclear data library
Above unintended process is difficult to find
  It is desirable to easily understand manual and warning message

## Slide 13: Enhancement of data output tool
Some drawing tools are prepared
  NJOY99 code has VIEWR tool for drawing the processed data
    Drawing tool is also used to compare the difference of the previous processed data
  The drawing tool only outputs the graph data
    The drawing tool doesn’t output the text data
Text data output tool is required to compare closely the difference by other programs
  The text data is appropriate to compare the difference using Excel, gnuplot or other programs

## Slide 14: Standardization of cross section data format
NJOY99 and NJOY2012 codes make some original nuclear data formats (PENDF and GENDF)
  The explanation of these data formats is not found in the manual
  The explanation of the intermediate and the final processed data format is desirable
These processed data format should be standardized
  The standardized processed data format is formulated by the GND project?

## Slide 15: FRENDY
The new nuclear data processing code of JAEA
  To fulfill all requirements mentioned above, JAEA has started developing a new nuclear data processing code, FRENDY, in 2013
The details of FRENDY will be presented at ND2016
  11-16, September, 2016, Bruges Belgium

## Slide 16: Conclusion
Answer of Questionnaire
Request for New Nuclear Data Processing Code
  Following the designation of the evaluated nuclear data library
  Enhancement of data output tool
  Standardization of cross section data format
Developing the new processing code, FRENDY
Thank you for your attention!!

## Slide 17: Calculation of the arbitrary temperature thermal scattering low (S(α,β)) data
The evaluated nuclear data library only prepare a few temperature S(α,β) data
  Users require the arbitrary temperature S(α,β) data
    Though users also require the arbitrary material S(α,β) data, it will not be scope of this meeting
Calculation function of the arbitrary temperature S(α,β) data is desirable