## Slide 1: Nuclear data processing with Fudge and GND
Consultant’s Meeting on Data Processing Capabilities
Caleb M Mattoon
Tuesday October 6, 2015

## Slide 2: FUDGE (For Updating Data and Generating Evaluations) provides nuclear data checking, fixing, manipulation and processing
Written primarily in Python, with extensions in c, c++ and Fortran for numerically intensive tasks
  Python interface facilitates both interactive and batch processing. FUDGE can be quickly integrated into other workflows
Originally written to handle Livermore’s legacy ENDL format and related tools
  this is ‘legacy’ FUDGE, of limited use except at LLNL
New FUDGE development focuses on Generalized Nuclear Data (GND)
  This part of FUDGE is capable of handling ENDF-6 (by translating to GND), will be useful to the broader nuclear data community

## Slide 3: FUDGE supports two-way translation between most ENDF-6 data and GND.
Types of data currently supported by translator:
  Incident neutrons, gammas, charged particles
  Fission product yields
  Photo-atomic, electron and atomic relaxation data
  Thermal neutron scattering (limited support)
Not yet supported:
  Decay sub-library
Test fidelity of translation by comparing original ENDF-6 with retranslated file
  Differences often indicate internal inconsistencies in original ENDF-6 files

## Slide 4: Once data are translated to GND, FUDGE supports several processing options:
Resonance reconstruction
Doppler broadening
Average energy/momentum deposition
Grouping
Generating transfer matrices
Data manipulation, physics checking, visualization
More details:

## Slide 5: Resonance reconstruction is built into Fudge, accelerated by NumPy and c extensions
Fudge supports (GND equivalents of) LRF=1,2,3 and LRF=7 with KRM=3 (Reich-Moore)
Reconstruction to user-specified accuracy
Results tested against RECENT and RECONR modules, found to be mostly in agreement (see next slide)
from fudge.gnd import reactionSuite
RS = reactionSuite.readXML(“n-017_Cl_035.gnd.xml”)
RS.reconstructResonances( styleName="reconstructed",
accuracy=0.001, thin=True )

## Slide 6: Sample comparison of FUDGE results with RECENT for ENDF-VII.1 evaluations:
Cl35 (n,p) cross sections (from LRF=7 reconstruction) agree to within 0.1%

## Slide 7: Sample comparison of FUDGE results with RECENT for ENDF-VII.1 evaluations:
Rh105 results differ in URR: target spins are inconsistent! ENDF claims 1/2 in RRR, 7/2 in URR
Different treatment of interpolation in unresolved region (PREPRO interpolates widths, Fudge interpolates cross sections)

## Slide 8: FUDGE development for other resonance parameter applications is ongoing
Elastic angular distributions from resonance parameters:
  complete for LRF=2 and 3, LRF=7 still TBD
Generating unresolved region probability tables
Thanks to Dave Brown for these contributions!

## Slide 9: Doppler broadening provided by the module ‘crossSectionAdjustForHeatedTarget’
Sample results compared to SIGMA1:
RS = reactionSuite.readXML(“n-094_Pu_239.gnd.xml”)
RS.reconstructResonances( … )
fissionXS = RS.getReaction(‘fission’).crossSection
heated = fissionXS.heat( RS, ‘600 K’, ‘1e-8 eV’ )

## Slide 10: Doppler broadening provided by the module ‘crossSectionAdjustForHeatedTarget’
Sample results compared to SIGMA1:
RS = reactionSuite.readXML(“n-094_Pu_239.gnd.xml”)
RS.reconstructResonances( … )
fissionXS = RS.getReaction(‘fission’).crossSection
heated = fissionXS.heat( RS, ‘600 K’, ‘1e-8 eV’ )

## Slide 11: FUDGE uses c library ‘numericalFunctions’ to handle 1-d XYs data and Legendre processing.
numericalFunctions capabilities:
  Add/subtract/multiply/divide 1-dimensional functions
    Automatically adds points to preserve user-specified accuracy when multiplying or dividing
  Switch interpolations (adding points as necessary)
  Integrate (grouping), convolute (Doppler broadening, Maxwellian averages)
  Calculate moments (average energy/momentum deposition)

## Slide 12: FUDGE uses c++ module ‘getTransferMatrix’ to generate deterministic transfer matrices
Produces transfer matrix for any reaction or decay product that has distributions specified
Handles all distribution types available in ENDF-6
Relativistic treatment for gammas (and other particles if requested by user)
Results for neutron products have been tested against NJOY and AMPX: helped identify issues in all three codes
Future work: test outgoing gamma matrices against other codes, implement corrections for thermal upscattering

## Slide 13: Transfer matrices: outgoing angle/energy spectra averaged over incident energy bins
Angular dependence is in Legendre expansion

## Slide 14: Transfer matrices: outgoing angle/energy spectra averaged over incident energy bins
Angular dependence is in Legendre expansion

## Slide 15: Processing codes don’t always agree, especially for double-differential distributions:

## Slide 16: Processing codes don’t always agree, especially for double-differential distributions:

## Slide 17: Processing codes don’t always agree, especially for double-differential distributions:

## Slide 18: For Monte Carlo applications, FUDGE defers most processing until run time
Resonance reconstruction and Doppler broadening are done before-hand
Grouping, generating cumulative distribution functions, equi-probable bins are computationally inexpensive
  Give users more flexibility by allowing them to change group structure, flux, etc. at run time
Monte Carlo application interface for GND (‘MCGIDI’) is being tested by LLNL’s Mercury developers
  TBD: support for angle biasing (for variance reduction)

## Slide 19: FUDGE provides tools to help evaluators improve the quality of nuclear data libraries
Physics checking
  Internal consistency (total cross section = sum of other reactions, Q-values match thresholds, …)
  Negative probabilities, un-normalized distributions
  Energy balance (raises many warnings for all existing libraries!)
Visualization
  plotEvals: plot same cross section for multiple evaluations (plus X4 and uncertainty band if available)
  compareCrossSections: two evaluations + relative difference
  Outgoing gamma spectra

## Slide 20: Gamma spectra in VII.1 are of mixed quality:
n + Pu239: discrete gammas at 1 MeV but not at thermal?

## Slide 21: Gamma spectra in VII.1 are of mixed quality:
n + P31: histogram-style spectrum?

## Slide 22: Future processing work at LLNL will be prioritized by needs of our users
Short term development goals:
  Finalize a version of GND, establish format governance
  Finish Monte Carlo API, implement deterministic API
  Expand tools to help check / fix nuclear data
  Migrate LLNL libraries to GND
Longer-term goals
  Support other institutions in migrating to GND
  Better treatment of thermal neutrons
  Multi-pole expansion for resonances, on-the-fly Doppler broadening