## Slide 1: 235U(n,f) cross section measurements for En < 12 eV by Deruytter and Wagemans
S. Kopecky, A. Plompen and P. Schillebeeckx
European Commission, Joint Research Centre (JRC), Geel (BE)
C. Wagemans
University of Gent (BE)
Neutron standards meeting, IAEA, Vienna, 6 – 10 December 2021

## Slide 2: 235U(n,f) cross section measurements
GELINA
MONNET
Absolute measurements at SCK CEN
EXFOR entry
Deruytter 1961, PhD Thesis and J. Nucl. En. 15 (1961) 165 DER61 20189 f(E)
Deruytter and Becker 1971, Nucl. Data for Reactors, Helsinki, 1971 DER73 f,0 , If
Deruytter 1973, J. Nucl. En. 27 (1973) 645 DER71a 20143 f,0, If
Relative measurements at GELINA
Deruytter and Wagemans, J. Nucl. En. 25 (1971) 263 DER71b 20131 f(E)
Wagemans et al., ND1979, Knoxville, p. 961 WAG79 21522 f(E)
Wagemans and Deruytter, IAEA-TECDOC-335, p. 156 WAG84 If
Wagemans et al., ND1988, MITO, p. 91 WAG88 22080 f(E)

## Slide 3: 235U(n,f): absolute cross section measurement, DER61
GELINA
MONNET
Chopper experiments at BR1 (2m FP) : velocity calibration by Bragg edges (Fe, Al, graphite, Be, Bi)
Energy dependence incident neutron beam :
K based on 197Au(n,) activation experiment : K = 2.708 (9) 10-3  (v0 = 2200 m/s, 1/v part) = 97.7 (5) b
Detection efficiency for fission fragments : f =0.888 (5)
Total number of 235U nuclides : Nf derived from m = 1.833 (10) mg 235U
  based on -counting using reference samples of same batch of material and produced under the same conditions
  No impact of T1/2 of 234U
combined uncertainty of (K, f, Nf) : 0.85%
  K : 0.33 %
  f : 0.56 %
  Nf : 0.55 %

## Slide 4: 235U(n,f): absolute cross section measurement, DER61
Data paper (see figure)
  f (v0 = 2200 m/s) = 586.5 (60) b
   (v0 = 2200 m/s, 1/v part) = 97.7 (5) b
Re-analysed using original data
  Separation correlated and uncorrelated uncertainty components
  197Au(n,) cross section from Dilg et al. (Z. Physik 264 (1973) 427)  (v0 = 2200 m/s, 1/v part = 97.73 (10) b) with  (v0 = 2200 m/s) = 98.68 (12) b
  f (v0 = 2200 m/s) = 586.7 (70) b
Data base Axton
  f (v0 = 2200 m/s) = 589.4 (78) b
GELINA
  Axton
  197Au(n,) :  (v0 = 2200 m/s) = 98.65 (9)b

## Slide 5: 235U(n,f): absolute cross section measurements, DER73
GELINA
MONNET
Chopper experiments at BR2 (2m FP) : velocity calibration by Bragg edges (Fe)
Energy dependence incident neutron beam, (n,r) :  (v0 = 2200 m/s) = 3835 (5) b
Total number of 10B nuclides : weighting and 10B(n,) experiments combined with chemical and isotopic composition from mass spec.
Total number of 235U nuclides : absolute -counting without calibration of reference samples from the same batch of material  influence T1/2 234U = 2.446 (4) x 105 a
Uncertainties due to systematic effects
  NB /NU : 0.38 %
  NB/NU without T1/2 234U : 0.35 %
  /f : 0.14 %
  10B(n,) : 0.13 %
  Velocity calibration : 0.02%
  total : 0.43 %
  without T1/2 234U : 0.40 %
   combined :

## Slide 6: 235U(n,f): absolute cross section measurements, DER73
Data paper
  f (v0 = 2200 m/s) = 587.6 (26) b
  If [0.02026, 0.06239] = 19.26 (8) b
  If [0.02, 0.06] not given and experimental data not available (yet)
Re-analysed
  10B(n,)  (v0 = 2200 m/s) = 3838 (6) b
  234U T1/2 = 2.455 (6) x 105 a (DDEP)
  f (v0 = 2200 m/s) = 585.4 (25) (present standards: 10B(n,)  (v0 = 2200 m/s) = 3844 (32) b  586.4 (53) b)
  If [0.02026, 0.06239] = 19.19 (8) b
  If [0.02, 0.06] = 18.75 (8) b (using If1/If1’ ratio from GELINA measurements, see further…)
Value in data base Axton
  f (v0 = 2200 m/s) x T1/2 = 1439.1 (64) b original data (incl. 10B) = 1438.4 (64) b
GELINA
  Axton
  197Au(n,) :  (v0 = 2200 m/s) = 98.65 (9)b
  10B(n,) :  (v0 = 2200 m/s) = 3838 (6) b
  234U : T1/2 = 2.457 (3) x 105 a
  Uncertainty
  Counting statistics : 0.15 %
  Systematic effects : 0.41 %
  10B(n,) :  (v0 = 2200 m/s) = 3835 (5) b
  234U : T1/2 = 2.446 (4) x 105 a

## Slide 7: 235U(n,f) absolute cross section measurements, DER61 & DER73
MONNET
EXFOR entry
Deruytter 1961, PhD Thesis and J. Nucl. En. 15 (1961) 165 DER61 20189 f(E)
Deruytter 1973, J. Nucl. En. 27 (1973) 645 DER71a 20143 f,0, If
  Deruytter (1961 & 1973) : 585.5 (24) b
  Axton (1986) : 585.1 (16) b
  Standards (2009) : 584.3 (10) b
  Standards (2017) : 587.3 (14) b
  JEFF-3.3 : 584.5 b
  ENDF/B-VIII.0 : 586.7 b
Deruytter et al. (1973)
= 19.19 (8) b
= 18.75 (8) b
  197Au(n,) :  (v0 = 2200 m/s) = 98.67 (10)b
  10B(n,) :  (v0 = 2200 m/s) = 3838 (6) b
  234U : T1/2 = 2.455 (6) x 105 a

## Slide 8: 235U(n,f): relative cross section measurements at GELINA
GELINA
MONNET
Experiments at GELINA:
Deruytter and Wagemans, J. Nucl. En. 25 (1971) 263 DER71b 20131 f(E)
Wagemans et al., ND1979, Knoxville, p. 961 WAG79 21522 f(E)
Wagemans and Deruytter, IAEA-TECDOC-335, p. 156 WAG84 If
Wagemans et al., ND1988, MITO, p. 91 WAG88 22080 f(E)
Details:
WAG 79, WAG 84: optimised for resonance integral relative to f(v = 2200 m/s)
WAG 88: optimised for sub-thermal energy region

## Slide 9: 235U(n,f): relative cross section measurements
GELINA
MONNET
Experiments at GELINA:
Deruytter and Wagemans, J. Nucl. En. 25 (1971) 263 DER71b 20131 f(E)
Wagemans et al., ND1979, Knoxville, p. 961 WAG79 21522 f(E)
Wagemans and Deruytter, IAEA-TECDOC-335, p. 156 WAG84 If
Wagemans et al., ND1988, MITO, p. 91 WAG88 22080 f(E) (dedicated to sub-thermal energy region!)
All data normalised to
 Cannot be used to determine

## Slide 10: Cross section at 2200 m/s or resonance integral
GELINA
MONNET
Example:
Cross section at 2200 m/s (based on fitting to data within same interval):
  Estimated value + propagating only uncorrelated uncertainties, e.g. due to counting statistics
Resonance integral:
  Estimated value + propagating only uncorrelated uncertainties, e.g. due to counting statistics
 No difference in relative uncertainty
Equal bin widths
=


## Slide 11: 235U(n,f): relative cross section measurements
Problems with data from Deruytter (1971), see also footnote in paper Wagemans (1984)
Using only data of Wagemans 1979, 1984 and 1988
  If3 / If1’ = 12.76 (8)
  If3 / If1 = 13.06 (8)
with If1’ = 19.19 (8) b eV from Deruytter 1973: If3 = 244. 7 (20) b eV
  197Au(n,) :  (v0 = 2200 m/s) = 98.67 (10)b
  10B(n,) :  (v0 = 2200 m/s) = 3838 (6) b
  234U : T1/2 = 2.455 (6) x 105 a

## Slide 12: Summary and conclusions
GELINA
MONNET
Cross section measurements from Deruytter and Wagemans were reviewed
absolute cross section data (at BR1 and BR2) are consistent and result in:
f(v = 2200 m/s) = 585.5 (24) b corresponding to
experiments at GELINA were performed relative to the cross section at v = 2200 m/s or If1 to determine the integral:
these GELINA data cannot be used to determine an absolute resonance integral e.g.
the GELINA data from 1971 in the EXFOR data base are not consistent with the results in the publication. Therefore they are not recommended to be used in an evaluation
An accurate determination of recommended cross section data, i.e. neutron standards, requires:
traceable data including a separation of uncertainties due to random and systematic effects
a careful study of experimental conditions (i.e. reading of related papers and reports) and uncertainty components
possible re-normalisation using improved/updated reference data (e.g. half-live of 234U)
cannot rely on automated procedures
= 244.7 (20) b eV
= 18.75 (8) b eV