## Slide 1
57Fe neutron inelastic scattering
The interplay between experiment and theory
A. Negret, C. Borcea, M. Boromiza, A. Olacel
Horia Hulubei National Institute for Physics and Nuclear Engineering, Bucharest-Magurele, ROMANIA
IAEA, December 2017
N. Nankov, A.J.M. Plompen, C. Rouki
European Comission, Joint Research Center, Geel, BELGIUM
Ph. Dessagne, M. Kerveno
CNRS, Universite de Strasbourg, UMR7178, IPHC, Strasbourg, FRANCE
M. Sin
University of Bucharest, Faculty of Physics, Bucharest-Magurele, ROMANIA
R. Capote
Nuclear Data Section, International Atomic Energy Agency, Vienna, AUSTRIA

## Slide 2
A. Negret – 57Fe(n,n’)
Summary
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions
IAEA, December 2017

## Slide 3
IAEA, December 2017
A. Negret – 57Fe(n,n’)
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions

## Slide 4
Why 57Fe?
IAEA, December 2017
A. Negret – 57Fe(n,n’)
Iron is an essential structural material for all nuclear installations.
Inelastic scattering is the main mechanism allowing neutrons to slow down.
At small energies the inelastic scattering occurs only on 57Fe.

## Slide 5
Why 57Fe?
IAEA, December 2017
A. Negret – 57Fe(n,n’)
Iron is an essential structural material for all nuclear installations.
Inelastic scattering is the main mechanism allowing neutrons to slow down.
At small energies the inelastic scattering occurs only on 57Fe.
When a natFe target is used, at high energies the 56Fe(n,ng) is “contaminated” by 57Fe(n,2ng):
56Fe + n
56Fe* + n
57Fe + n
56Fe* + 2n
when En > Sn(57Fe) = 7.6 MeV

## Slide 6
IAEA, December 2017
A. Negret – 57Fe(n,n’)
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions

## Slide 7
Experimental setup and method
IAEA, December 2017
A. Negret – 57Fe(n,n’)
Pulsed neutron source
GELINA of EC-JRC Geel
Electron linac (140 MeV) + 238U target
Pulse width ~1 ns
Repetition rate: 800 Hz
Energy range: 0 – 20 MeV
Gamma flash from
bremsstrahlung
Flight path: 200 m
(~550 neutrons/cm2s)
Neutron source
200 m flight path
Sample to be measured +
detection system GAINS

## Slide 8
Experimental setup and method
IAEA, December 2017
A. Negret – 57Fe(n,n’)
GAINS: Gamma array for Inelastic neutrons scattering
12 HPGe detectors, able to measure:
Very precisely the energy of g rays
The time of g rays with a precision of 10 ns => neutron energy
One Fission Chamber (235U) for beam monitoring
g-production cross sections.
Then, knowing the level scheme, we determine:
Level cross sections
Total inelastic cross section.
Experimental method: g spectroscopy + time of flight
Primary experimental result:

## Slide 9
IAEA, December 2017
A. Negret – 57Fe(n,n’)
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions

## Slide 10
57Fe: the problems
IAEA, December 2017
A. Negret – 57Fe(n,n’)
expensive, very thin target (this is also the
case for 54Fe).
Issues:
first level at 14 keV.
conversion coefficient a = 8.5(3)
level half-life T1/2 = 98.3(3) ns

## Slide 11
g spectroscopy at 14 keV
IAEA, December 2017
A. Negret – 57Fe(n,n’)
14 keV
7 keV

## Slide 12
IAEA, December 2017
A. Negret – 57Fe(n,n’)
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions

## Slide 13
g-production cross sections
IAEA, December 2017
A. Negret – 57Fe(n,n’)

## Slide 14
IAEA, December 2017
A. Negret – 57Fe(n,n’)
What is missing?
The first transition (14.4 keV) could not be observed.
The total inelastic cross section could not be built.

## Slide 15
Called a theoretician: “Help!”
IAEA, December 2017
A. Negret – 57Fe(n,n’)
If a consistent calculation could reproduce perfectly the g-production cross sections that we measured then perhaps we could also trust the 14.4-keV g-production cross section.

## Slide 16
Tuned EMPIRE calculations
IAEA, December 2017
A. Negret – 57Fe(n,n’)
1. The nonelastic cross section was adjusted with an energy dependent factor (0.7 @ 0.1 MeV – 1 @ 3 MeV) in order to correct the optical model prediction.
2. Some level population cross sections were adjusted to compensate for the impossibility of considering a large number of transitions between discrete levels. This adjustment may also compensate for possible deficiencies of the level scheme (wrongly assigned Jp or branching ratios)

## Slide 17
Total inelastic cross section…
IAEA, December 2017
A. Negret – 57Fe(n,n’)
… obtained as an interplay between experiment and theory

## Slide 18
One more word:
the theoretical total inelastic cross section
IAEA, December 2017
A. Negret – 57Fe(n,n’)

## Slide 19
IAEA, December 2017
A. Negret – 57Fe(n,n’)
57Fe: why?
Experimental setup
Specific difficulties
Results
Conclusions

## Slide 20
Conclusions
IAEA, December 2017
A. Negret – 57Fe(n,n’)
We performed a 57Fe(n,n’) cross section measurement using g spectroscopy,
The first transition in 57Fe, Eg=14.4 keV remained inaccessible,
We called a theoretician and asked for help,
The theoreticians did their best and tuned EMPIRE predictions on the experimentally determined g-production cross sections,
We generated a kind of hybrid nuclear data, as an interplay between experiment and theory,
We still wish to measure the 14.4-keV transition:
  57Fe(p,p’g) at IFIN-HH,
  57Fe(n,n’g) at JRC-Geel, with planar detectors.

## Slide 21
One word on 16O inelastic: 16O(n,n’) and 16O(p,p’)
IAEA, December 2017
A. Negret – 57Fe(n,n’)
PRELIMINARY DATA
Eg = 6128.6 keV
16O(n,n’g) 16O(p,p’g)