## Slide 1: On Cross Section Correlations, Uncertainty Reduction and Calibration from Integral Data
A.Trkov, R.Capote, O. Cabellos
IAEA, Vienna, Austria
ETSII/UPM Madrid, Spain

## Slide 2: Background
Current IAEA CIELO covariances based on measured differential data lead to large uncertainties in criticality benchmarks (keff~1-2%)
Small calibration of mean values have been employed to improve C/E without changing ND uncertainties
Close alignment with benchmark values does not mean low uncertainty (e.g., HEU bare assemblies have a spread of ~1.5% in spite of quoted low uncertainties)
Some correlations are not present in differential data, but appear only when integral data are introduced
  e.g., nu-bar and fission cross section
  Such correlations are (likely) benchmark-dependent
  Such correlations reduce keff

## Slide 3: Model
Consider a grossly simplified 1-group toy model of a criticality benchmark:
f=fission; c=capture; i=inelastic, L=leakage
Consider 3 benchmarks:
  Godiva (<E>=700 keV, very hard spectrum)
  Big_Ten (<E>=40 keV, hard spectrum)
  HISS (<E>=1 keV, soft intermediate spectrum)
Eq. (1):

## Slide 4: Godiva

## Slide 5: Big Ten

## Slide 6: HISS

## Slide 7: Simple model input data
 | Godiva | Big_Ten | HISS
Σf [b] | 3.22379 | 3.40604 | 21.43619
 | 2.59155 | 2.48734 | 2.42695
Σf [b] | 1.24396 | 1.36935 | 8.83258
Σc [b] | 0.14236 | 0.27764 | 4.42019
Σi [b] | 1.61269 | 1.06276 | 0.55585
Δ [%] | 0.50 | 0.50 | 1.00
ΔΣf [%] | 1.21 | 1.21 | 0.26
L | 0.22390 | 0.68086 | 7.30392
keff (MC) | 1.00027 | 1.00445 | 1.01533
Δkeff (exp) [pcm] | 200 | 140 | 800
keff (exp) | 1.00000 | 1.00455 | 1.00000
Cross sections averaged over benchmark spectra and the corresponding uncertainties were calculated with the RR-UNC code using “e80b4” data and MCNP calculated benchmark spectra. The keff uncertainties are 2-sigma benchmark values.

## Slide 8: Simple model-based correlations (due to integral benchmark data)
Corr. Coef.  -Σf | Godiva | Big_Ten | HISS | E-range
Total | -0.929 | -0.963 | -0.189 | Full range
Fast | -0.928 | -0.963 | -0.306 | E[>1MeV]
Epi-Hi | -0.928 | -0.963 | -0.487 | E[1keV:1MeV]
Epi-Lo | -0.955 | -0.926 | -0.167 | E[1eV:1keV]
Thermal | -0.180 | -0.180 | -0.180 | Standards-2017
Correlation coefficients are calculated with cross sections averaged over different parts of the spectrum as indicated.
The thermal value is taken from Standards-2017.
Correlations are derived from Monte Carlo sampled keff using Eq.(1)
with the integral constrain that keff(sampled) = keff(MC) ± Δkeff (exp) ).rnd
where rnd is a random number in the range [-1:1]

## Slide 9: Reduction in uncertainties (due to integral benchmark data)
Energy range | Godiva [%] | Big_Ten [%] | HISS [%] | Differential (Initial)[%]
Total | 0.29 | 0.29 | 0.46 | 0.50
Fast | 0.29 | 0.29 | 0.27 | 0.50
Epi-Hi | 0.29 | 0.29 | 0.49 | 0.50
Epi-Lo | 0.39 | 0.21 | 0.46 | 1.00
Energy range | Godiva Σf [%] | Big_Ten Σf [%] | HISS Σf [%] | Differential (Initial)Σf[%]
Total | 0.51 | 0.50 | 0.15 | 1.21
Fast | 0.49 | 0.47 | 0.64 | 1.22
Epi-Hi | 0.52 | 0.51 | 0.52 | 1.22
Epi-Lo | 0.64 | 0.34 | 0.13 | 1.10

## Slide 10: Reduction in k_eff uncertainties
Uncertainty estimates with NDaST before and after the introduction of - correlations in U-235
k_eff Uncertainty |  | 
 | Initial | Final
Godiva | 1043 | 868
Big_Ten | 1099 | 949
HISS | 649 | 263

## Slide 11: Dependence on mean values (calibration effect)
The HISS benchmark has an offset of ~1500pcm in the calculated keff
Calibrating keff to 1 (changing the evaluation mean values to get keff=1, while preserving uncertainties) has a minimal effect on derived uncertainties and correlations for cross sections (“adjusted”)
Increasing the mean value of  by 0.2% without changing the uncertainty has a similarly negligible effect on uncertainties and correlations

## Slide 12: Dependence on mean values (HISS)
Corr. Coef.  -Σf | k-eff=1 | +0.2% | Nominal | E-range
Total | -0.188 | -0.188 | -0.189 | Full
Fast | -0.298 | -0.298 | -0.306 | E[>1MeV]
Epi-Hi | -0.479 | -0.479 | -0.487 | E[1keV:1MeV]
Epi-Lo | -0.166 | -0.166 | -0.167 | E[1eV:1keV]
 [%] | k-eff=1 | +0.2% | Nominal | Differential (Initial) [%]
Total | 0.47 | 0.47 | 0.46 | 0.50
Fast | 0.27 | 0.27 | 0.27 | 0.50
Epi-Hi | 0.49 | 0.49 | 0.49 | 0.50
Epi-Lo | 0.47 | 0.47 | 0.46 | 1.00
Σf [%] | k-eff=1 | +0.2% | Nominal | Differential (Initial) [%]
Total | 0.15 | 0.15 | 0.15 | 1.21
Fast | 0.64 | 0.64 | 0.64 | 1.22
Epi-Hi | 0.52 | 0.52 | 0.52 | 1.22
Epi-Lo | 0.13 | 0.13 | 0.13 | 1.10

Implicit correlations due to calibration are negligible !!

## Slide 13: Observations on to correlations
Correlations are different for different critical systems
Correlations are energy-dependent
There exists some similarity between different systems
Uncertainties of and also undergo a significant reduction
Uncertainties and correlations are insensitive to changes in the evaluated mean values, no implicit (hidden) correlations are observed

## Slide 14: Conclusions
Introducing correlations from considering experimental integral constrains (criticality benchmarks) may reduce the calculated uncertainties but:
Correlations depends on selected benchmark
Due to benchmark-dependence additional correlations (and reduced parameter uncertainties) should only be applied in derived files
(Small) changes to mean values (calibrations) do not introduce correlations – these are introduced only when new information is added (e.g. integral experiment data)