## Slide 1: Evaluating multipole mixing ratio from conversion electron data
Tibor Kibèdi
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop

## Slide 2: Conversion coefficients
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Transition probability
  lT = lg + lK + lL + lM…… + lp
Conversion Coefficient
Electron conversion
g-ray
K
L
M
e- - e+
pair
Mixed transition
or using the Mixing ratio
Special class: M1+E2+E0 …

## Slide 3: Using BrIcc
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Put all BrIcc and BrIccMixing files into one directory
Include this folder into the “PATH” variable
Set the “BrIccHome” variable to point to this folder
Windows installation script will do it automatically
Use the “SET” command to verify these settings
BrIcc and BrIccMixing are console applications and should run from a console terminal window from any directory
Always use the latest version!
Basic help can be obtained by “bricc ?” and “briccmixing ?”
Examine - calculation report file (“BrIcc.lst”)
  - records to be INSERTED, DELETED or
  REPLACED (“Cards.new”)

## Slide 4: BrIcc - Calculation report
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Can be changed

## Slide 5: BrIcc – new cards
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Versions since 31-Mar-20008
9-Jul-2008, 20-Jan-2009, 19-Oct-2009, 18-Apr-2011, 13-Aug-2011, 9-Oct-2012, 29-Mar-2013, 28-Jun-2013, 7-Aug-2013,
16-Dec-2014

## Slide 6: BrIcc – new cards
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
CC-DCC_L overlaps with ZERO
Non-Physical
Balraj Sing (26-Sep-2012)
6.5E+6 50
in ENSDF

## Slide 7: Check uncertainties 34(5) keV E4 transition in 211Po
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop

## Slide 8
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
aT = 1.53E6 (35+5 keV)
CC = 3.87E6 (34 keV)
aT = 1.16E7 (35-5 keV)
CC±DCC overlaps with zero!
How BrIcc handles uncertainties 34(5) keV E4 transition in 211Po

## Slide 9: How BrIcc handles uncertainties 34(5) keV E4 transition in 211Po
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
aT = 1.53E6 (34+5 keV)
CC = 3.87E6 (34 keV)
aT = 1.16E7 (34-5 keV)
Log scale

## Slide 10: How BrIcc handles uncertainties 34(5) keV E4 transition in 211Po
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
aT = 1.53E6 (35+5 keV)
CC = 3.87E6 (34 keV)
aT = 1.16E7 (35-5 keV)
Log scale
CC = [1.16E7 + 1.53E6] / 2
CC = 6.57E+6
DCC = [1.16E7 - 1.53E6] / 2
CC = 5.04E+6
Adopt CC= 6.6E+6 50
Edit “Cards.new” before running
“bricc 211Po_IT.ens merge”
6.5E+6 50
in ENSDF

## Slide 11: How BrIcc handles uncertainties 1754.9(6) keV M1+E2 transition in 16O
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Pure
mixed
Unc from MR
Unc from E
CC < 1E-4 !

## Slide 12: Using BrIccMixing
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
BrIccMixing can be used to determine the ABSOLUTE value of the multipole MIXING RATIO, “MR”
BrIcc and GnuPlot (http://www.gnuplot.info) to be installed
Available on myENSDF
Accepts various types of measured data with symmetric uncertainties; free format, NDS uncertainties:
  “NSR-key”(max 20 char) “SHELL” “VAL” “UNC” “TYPE”
  1968GeZW L1/L3 23.0 16 R
  Conversion coefficients (Absolute values, A):
      K, L2, M23 (M2 + M3)
  Ratios of conv. coeff. or intensities (Relative values, R):
      K/L, L12/M34 ([L1+L2]/[M3+M4])
  Mixing ratios(Absolute values, A):
      MR

## Slide 13: BrIccMixing – Input file
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Titile
Transition to load BrIcc table and
Specity multipolarity
Comments
New dataset

## Slide 14: Running BrIccMixing
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
briccmixing 99Tc_BrIccMixing.in :
Method of solution
(a) CFIT 1980Ry04
(b) Searching Χ2/ν v.s. MR
  hyper surface
Find Χ2/ν minimum  MR
Find DMR_L & DMR_H where
  Χ2/ν risen by 1

## Slide 15: Running BrIccMixing
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
Find minimum, but no lower limit

## Slide 16: Measuring conversion coefficients
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop

## Slide 17: Measuring conversion coefficients
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop
1952He18 reported EKC=XPG; 0.095 5
  Assuming WK(Ba)=0.87 1
Using WK (Ba)=0.900 4 (1996SCo6)
EKC=0.092 5

## Slide 18: Measuring conversion coefficients see In Proc. Internal Conversion Process, ed.by Hamilton, J.H., North-Holland, 1975
Tibor Kibèdi, Dep. of Nuclear Physics, Australian National University
28-Apr-2015, IAEA NSDD Workshop