## Slide 1: The CMAM “Centro de Micro Análisis de Materiales” Universidad Autónoma de Madrid
Presented by: Ángel Muñoz-Martin
Meeting of the CRP
“Development of a Reference database for Particle Induced Gamma ray Emission (PIGE) Spectroscopy”
Vienna 16-20 may 2011

## Slide 2
UAM
Mailing Address Centro de Microanálisis de Materiales Calle de Faraday 3, Universidad Autónoma de Madrid Campus de Cantoblanco E-28049, Madrid, Spain
Phone number (+34) 91 497 3621 (Switchboard)
Fax number (+34) 91 497 3623
Email Address cmam@uam.es
WEB page
http://www.cmam.uam.es
Notes: The campus is CEI

## Slide 3: Research areas
Nanoscience and Advanced Materials
  41 groups located at or near the UAM+CSIC Campus. 9 of the 20 most relevant condensed matter physicists in Spain (H index above 32)
Biology and Biomedicine
  Largest scientific community in Spain (and one of the largest in Europe) devoted to Biology, Biomedicine and Biotechnology
Theoretical Physics and Mathematics

## Slide 4
CMAM is a research facilty @ CEI UAM-CSIC
60% for CMAM scientific personnel doing their own research and developing new Ion beam techniques
40% beamtime for external research institutions and private companies

## Slide 5
MATERIALS
Advanced materials
Energy
Health
C. Heritage
Cooperation

## Slide 6: Staff
A staff of 23:
10 scientists,
3 PhD students,
8 technicians,
2 administrative

## Slide 7: 5MV Tandem accelerator
Very low ripple <50V @ 5MV
2 ion sources:
  Duoplasmatron
  Sputtering
Chart: 
| Au | Br | C | H | He | Si | F | Cl | B | O | Pb | B2 | Br
Total | 8 | 13 | 3 | 61 | 63 | 5 | 6 | 8 | 2 | 4 | 3 | 7 | 1
Notes: First Coaxial High Current Tandetron Accelerator using the Cockcroft-Walton power supply system to reach 5MV

## Slide 8: Beamlines
Standard
External m-beam
ERDA-ToF
Nuclear Physics
Under commissioning
  Implantation,
  UHV-line,
  Internal m-beam

## Slide 9
Chart: 2010 Beamline use
| ACC | IuB | IMP | TOF | STD | EuB | NUC
Total | 7 | 60 | 37 | 33 | 210 | 91 | 2
Chart: 2010 accelerator use
| Maintenance | Comissioning | Beamtime
 | 87 | 104 | 331
Time distribution | 2009 |  | 2010 | 
Usable shifts | 644 |  | 600 | 
Reallocated from previous periods | 68 |  | 17 | 
Maintenance shifts | 118 |  | 96 | 
Buffer shifts | 60 |  | 71 | 
Reserved comissioning shifts | 69 |  | 60 | 
Available shifts | 329 | 526 | 356 | 504

## Slide 10: Standard beamline
Classical IBA techniques
(RBS, RBSc, ERDA, NRA)
IBMM over small areas

## Slide 11: Standard beamline
In vacuum chamber
4 axis goniometer
Two charged particles detectors (fixed & movable). For the movable one it is possible to define different solid angles and change absorber foils.
A high sensitivity optical camera
A special viewport for far-infrared (thermal) camera
A few ports are available for coupling a HPGe detector for gamma rays.

## Slide 12: Measurements of g-ray emission induced by protons on fluorine and lithium
A.Caciolli, G.Calzolai, M.Chiari, A.Climent-Font, M.T.Fernández , G.Garcia F.Lucarelli, S.Nava, A.Zucchiatti Nucl. Instr. & Meth.B249(2006)98-100

## Slide 13: Proton elastic scattering and proton induced g-ray emission cross-sections on Na from 2 to 5 MeV
A.Caciolli, G.Calzolai, M.Chiari, A.Climent-Font, G.Garcia, F.Lucarelli, S.Nava Nucl. Instr. & Meth.B266(2008)1392-1396

## Slide 14: Quantification of sodium in ancient Roman glasses with ion beam analysis
Depth profiling of Na by changing energy of the beam and comparing with a NIST standard

## Slide 15: External mbeam
Used mainly to perform IBA in art and archaeology
Environmental and material science studies have occasionally been done

## Slide 16: External mbeam
2 X-ray detectors for the PIXE,
1 silicon implanted blind detector, in Cornell geometry, for RBS.
For the PIGE a HPGe and a LaBr3 detectors can be installed temporarily.
The beam is extracted in air through a 0.2 μm thick Si3N4. In regular operation beams around 30 μm diameter are obtained.
The sample movement and position are remotely controlled

## Slide 17: Detection of beryllium treatment of natural sapphires by NRA
The simple and non-destructive method for evidencing Be-treatment proposed here relies on the
9Be(a, ng)12C nuclear reaction using a helium ion beam impinging on the gem placed in air and recording the 4439 keV prompt g-ray tagging Be atoms.
P.C.Gutierrez, M.D.Ymsa, A.Climent-Font, T.Calligaro Nucl. Instr. & Meth.B268(2010)2038-2041
Notes: In the case of a sapphire target, the cray spectrum also shows a 2235 keV line produced by aluminium through the 27Al(a, pc)30Si reaction [9,10] which can conveniently be used as a monitor of the integrated beam charge. However, the energy of the impinging He ions has to be carefully adjusted since in sapphires, due to the poor resolution of the scintillator detector used in the experiment, the 3498 keV c-rays from the decay from the second level of 30Si in the previous reaction might interfere with the searched 4439 keV c-rays.

## Slide 18: Nuclear Physics beamline
In cooperation with Spanish National Research Council (CSIC)
Used mainly for Nuclear Astrophysics and testing of new detectors
High flexibility
at the end station

## Slide 19: Time of Flight
Mainly used for ERDA on thin films
ToF and Energy are measured for each particle in coincidence
No overlapping
of elements

## Slide 20: Extension of ToF beamline
A new high vacuum chamber has been added to ToF beamline
Chamber is electrically isolated (Faraday cup)
Top flange is exchangeable allowing for easy setup of experiments
Two g rays detectors have been installed
Acquisition software can register data in list mode
Continuous record of actual current and dose
…

## Slide 21: Participation in the CRP
Taking advantage of the 5MV to explore higher energies
Focus in Li, Be and F (fusion reactor materials, gemstones & environmental)
Beams: p and a